## Slide 1
ArduSub + Gazebo
A beginner guide to the virtual ROV
Controls, physics, maps, modes, and the files behind them
Notes: Based on the local ArduPilot checkout and docs/bluerov-gazebo/README.md. The models are schematic teaching models, not validated physical BlueROV replicas.

## Slide 2
What each program does
2
QGroundControl
Pilot screen: virtual joystick, flight mode, map, and depth readings.
MAVProxy
Relays MAVLink commands and telemetry between QGC and ArduSub.
ArduSub SITL
Runs the autopilot code on your computer instead of a flight controller.
Gazebo
Applies thruster forces and computes movement in a 3D world.
Notes: Sources: /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/README.md; /Users/rafaelgarcia/ardupilot/ArduSub; /Users/rafaelgarcia/ardupilot/libraries/SITL/SIM_JSON.cpp. SITL means software in the loop. QGroundControl is the ground control station (GCS).

## Slide 3
What the current model simulates
3
INCLUDED
ROV motion in water
Thruster forces from ESC commands
Buoyancy and drag
IMU and position data sent to SITL
SIMPLIFIED OR MISSING
Box shaped body and approximate mass
Placeholder drag values
No camera, tether, or water current
No embedded architecture faults
Use these models to learn the control path and check directions. They are not validated ROV designs.
Notes: Source: /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/README.md, especially Limits before using these models for design decisions. Generated model SDF contains mass, thruster and hydrodynamics settings.

## Slide 4
The control loop
4
QGroundControl
Joystick and mode
MAVProxy
MAVLink relay
ArduSub SITL
Motor mixing
Gazebo
Forces and motion
Gazebo sends simulated position and IMU data back to ArduSub.
ArduSub sends MAVLink telemetry to QGroundControl.
Notes: Source: /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/README.md, section How ArduSub and Gazebo are connected. The ArduPilotPlugin exchanges JSON with SITL over UDP 9012; MAVProxy uses SITL TCP 5770 and QGC UDP 14660.

## Slide 5
One downward stick command
5
1
QGC sends
MANUAL_CONTROL z = 250
2
ArduSub sees
RC channel 3 = 1400
3
Vertical motors 5 and 6
receive PWM 1600
4
Gazebo applies force
and the ROV descends
Measured in the isolated BlueROV2 test: altitude went from −0.01 m to −0.52 m.
Notes: Source: /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/README.md, Vertical-direction check after the fix. Values are from one isolated test, not calibrated thrust or speed performance.

## Slide 6
Manual mode and Depth Hold
6
MANUAL
The stick commands vertical thrust.
Release the stick: thrust returns to neutral. The ROV may stay at its new depth or drift.
DEPTH HOLD
The autopilot uses a depth estimate.
Release the stick: it tries to maintain the current depth.
Neither mode automatically returns the ROV to the surface.
Notes: Sources: /Users/rafaelgarcia/ardupilot/ArduSub/mode_manual.cpp and /Users/rafaelgarcia/ardupilot/ArduSub/mode_althold.cpp. ModeManual::run passes normalized pilot throttle to the motors. ModeAlthold uses vertical position control.

## Slide 7
Why the ROV stays submerged
7
The current Gazebo model is nearly neutrally buoyant.
ROV mass
12 kg
Water displaced
0.012 m³ × 1000 kg/m³ = 12 kg
Weight and buoyancy approximately balance. Neutral thrust gives little reason to rise.
Notes: Sources: /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/generated/worlds/bluerov2.sdf for water density 1000 kg/m^3 and volume 0.012 m^3; /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/generated/models/bluerov2_test/model.sdf for total mass 12 kg (11.988 kg body plus six 0.002 kg thrusters). Idealized balance; numerical drift and other forces can remain.

## Slide 8
Startup sequence on this Mac
8
1 Gazebo
Loads the generated BlueROV2 world and listens on UDP 9012.
2 SITL launcher
Starts ArduSub with JSON physics, vehicle ID 2, and Jervis Bay home.
3 MAVProxy
Connects to SITL on TCP 5770 and sends data to QGC on UDP 14660.
4 QGC
Connects to vehicle 2; the virtual joystick sends pilot input.
On macOS, the Gazebo server and Gazebo window start separately.
Notes: Source: /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/README.md, Run one layout on this Mac. The launcher script is /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/launch_sitl_gui.sh. The built-in sim_vehicle.py launcher can stop other SITL processes on this Mac at exit, so the convenience script checks for them.

## Slide 9
The QGroundControl map
9
Home location: Jervis Bay, Australia
−35.1192416°, 150.7296753°
The map plots the latitude and longitude ArduSub reports.
Gazebo shows a generic ocean scene, not a 3D copy of Jervis Bay.
Depth appears in telemetry; a flat map cannot show underwater scenery.
Notes: Sources: /Users/rafaelgarcia/ardupilot/Tools/autotest/locations.txt (Jervis_Bay); /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/README.md. The generated world has no geographic terrain or shoreline.

## Slide 10
The three frame choices
10
BlueROV1
6 motors
Six controllable axes in the idealized model; some coupling.
BlueROV2
6 motors
No direct pitch control in the stock vectored mixer.
BlueROV2 Heavy
8 motors
Four vertical thrusters add direct pitch control.
These are schematic models. Match mass, thrust curves, and drag to hardware before comparing designs.
Notes: Sources: /Users/rafaelgarcia/ardupilot/libraries/AP_Motors/AP_Motors6DOF.cpp; /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/README.md and verify.py. BlueROV1 and Heavy rank 6; BlueROV2 rank 5 in the idealized force allocation. Static mapping passed for all three; dynamic down/up retest after the vertical correction was performed only for BlueROV2.

## Slide 11
Code files: the Gazebo side
11
generated/worlds/
bluerov2.sdf
Water density, displaced volume, and which model the world loads.
generated/models/
bluerov2_test/model.sdf
Thruster placement, motor topics, and the ArduPilotPlugin connection.
generate.py
Creates the three model layouts and their parameter files.
launch_sitl_gui.sh
Passes Jervis Bay, JSON physics, frame parameters, and MAVProxy settings.
Open these under docs/bluerov-gazebo/
Notes: Full paths are under /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/. In the model SDF, inspect ArduPilotPlugin, fdm_port_in, control channel, and cmd_topic. In the world SDF, inspect uniform_fluid_density and set_volume.

## Slide 12
Code files: the ArduSub side
12
ArduSub/joystick.cpp
Converts MAVLink MANUAL_CONTROL into pilot channel inputs.
ArduSub/
mode_manual.cpp
Shows what Manual mode sends to the motors.
ArduSub/
mode_althold.cpp
Shows how Depth Hold controls vertical motion.
libraries/AP_Motors/
AP_Motors6DOF.cpp
Defines the motor mixing factors for each frame.
Also inspect libraries/SITL/SIM_JSON.cpp for the external physics data exchange.
Notes: Sources: the named files in /Users/rafaelgarcia/ardupilot. Look for transform_manual_control_to_rc_override in joystick.cpp, ModeManual::run, ModeAlthold::run, and add_motor_raw_6dof in AP_Motors6DOF.cpp.

## Slide 13
A short exercise to try
13
1 Start
Run Gazebo, then the SITL launcher, then connect QGC to vehicle 2.
2 Dive
In Manual, move the depth stick down briefly and watch altitude fall.
3 Release
Let the stick center. Notice that the ROV stays near its new depth.
4 Compare
Switch to Depth Hold. Move slightly, release, and watch it hold depth.
Change one setting at a time and write down what the telemetry actually shows.
Notes: Source: /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/README.md. The steps are for the virtual vehicle only. QGC uses the separate UDP 14660 link for the Gazebo-backed SITL instance.

## Slide 14
Terms to remember
14
SITL
Software in the loop: ArduSub runs on the computer.
MAVLink
Messages carrying pilot commands and vehicle telemetry.
Frame
The motor layout and mixing rules ArduSub uses.
SDF
The file format that describes a Gazebo world or model.
Notes: Sources: /Users/rafaelgarcia/ardupilot/docs/bluerov-gazebo/README.md; /Users/rafaelgarcia/ardupilot/Tools/autotest/sim_vehicle.py; /Users/rafaelgarcia/ardupilot/libraries/AP_Motors/AP_Motors6DOF.cpp. Definitions simplified for beginners.