## Slide 1
BlueROV task package
A beginner’s code review of the nine staged files
ArduSub SITL + Gazebo · macOS package · current staged state
Notes: Source: the nine staged files in /Users/rafaelgarcia/ardupilot, inspected on the local main branch. This deck explains the current staging area, not every file in the repository. The package provides schematic BlueROV models for learning and preliminary comparisons. Nothing in the slide deck establishes real ROV performance.

## Slide 2
What the simulation connects
THE BIG PICTURE
Pilot and autopilot
Physics and feedback
QGroundControl shows the virtual ROV and sends joystick commands.
ArduSub SITL turns a requested motion into motor outputs using its selected frame mixer.
Gazebo calculates how the model moves.
The connector carries motor commands into Gazebo and sends simulated state back to ArduSub.
Notes: Source: docs/bluerov-gazebo/generate.py, run_gazebo_mac.sh, launch_sitl_gui.sh. QGroundControl sends pilot commands to ArduSub. ArduSub runs the same autopilot control code used in SITL and produces motor outputs. The ArduPilot Gazebo connector publishes those outputs to Gazebo motor topics and returns simulated pose, velocity, and IMU readings. Gazebo calculates model motion. Each program can run on the same Mac; separate Terminal windows do not mean separate computers. The model is schematic, so the result is a controlled software experiment.

## Slide 3
The nine staged files
FILE INVENTORY
Current BlueROV path
Run and earlier experiment
.gitignore
prepare_mac.sh
rov-sim-macos.patch
beaumont-ardupilot-gazebo-test.patch
generate.py
verify.py
run_gazebo_mac.sh
launch_sitl_gui.sh
beaumont-gazebo-prepare-test.py
Earlier Beaumont connection experiment only
Notes: Source: git diff --cached --name-only. Four files build or check the model, two files start the simulation, two are dependency patches, and one is a historical Beaumont helper. The helper is not called by the current BlueROV path. .gitignore prevents local builds and generated worlds from being staged.

## Slide 4
.gitignore: keep local output local
FILE 1 OF 9
/generated/
/.local/
/.deck-build/
/__pycache__/
The source files can travel through Git. Built libraries and generated worlds depend on each member’s Mac, so the setup script recreates them locally.
Notes: Source: docs/bluerov-gazebo/.gitignore. The four rules exclude generated/, .local/, .deck-build/, and __pycache__/ only under the BlueROV package directory. generated/ is excluded because each SDF contains an absolute path to a locally built connector library. .local/ holds external cloned sources and compiled plugins. .deck-build/ holds temporary slide authoring files. __pycache__/ is Python's bytecode cache. This file does not ignore the generator or launcher source.

## Slide 5
prepare_mac.sh: what it checks first
FILE 2 OF 9
Inputs it expects
Why this matters
macOS
Gazebo, Git, CMake, Python
Built ArduSub SITL binary
No existing generated/ folder
A missing dependency stops with a direct error.
The script keeps previously generated worlds intact instead of silently replacing them.
Notes: Source: docs/bluerov-gazebo/prepare_mac.sh lines 1–29. set -euo pipefail stops on failed commands, undefined variables, and failed pipeline elements. The script computes repo_root from its own location so it can be called from another directory. It checks macOS, required commands, and an existing ArduSub SITL binary. It refuses to overwrite generated worlds. This protects a working local setup but means a member must move an old generated/ directory aside before a new preparation run.

## Slide 6
prepare_mac.sh: what it creates
FILE 2 OF 9
1 Clone two pinned dependencies into .local/
2 Apply both included patches
3 Build four Gazebo plugin libraries
4 Generate three BlueROV worlds and parameter files
5 Run static verification
Notes: Source: docs/bluerov-gazebo/prepare_mac.sh lines 31–73. It clones rov-sim at 3597a5c and ardupilot_gazebo at 082a0fe into ignored .local/. It applies the two patches and verifies their reverse application to detect mismatched local checkouts. It builds the Gazebo buoyancy, hydrodynamics, and thruster plugins plus ArduPilotPlugin. It calls generate.py to write worlds/models/parameter files and verify.py to check the result. The pinned revisions help repeat the experiment, but the full setup script has not been re-run from a fresh Mac in this task.

## Slide 7
rov-sim-macos.patch: build support
FILE 3 OF 9
+ find_package(Qt5 REQUIRED
+ COMPONENTS Core Gui Widgets)
CMake is the build recipe. This one-line patch helps the Gazebo plugin build find Qt on macOS. The generated model still supplies the ROV geometry.
Notes: Source: docs/bluerov-gazebo/rov-sim-macos.patch. This patch adds find_package(Qt5 REQUIRED COMPONENTS Core Gui Widgets) to the pinned rov-sim CMakeLists.txt before gz-sim8 is found. It is applied to the private .local/rov-sim checkout, not to this ArduPilot repository. On the tested Mac, it supplies an explicit Qt dependency for CMake configuration. It does not change thruster physics or the ROV frame.

## Slide 8
Connector patch: match the ESC message
FILE 4 OF 9
Before: Advertise<msgs::Double>()
After: Advertise<msgs::Int32>()
Before: cmd.set_data(value)
After: cmd.set_data(lround(value))
Gazebo topics have a type. A publisher using Double and a subscriber expecting Int32 cannot exchange the motor command as intended.
Notes: Source: docs/beaumont-ardupilot-gazebo-test.patch. The patch adds an Int32 Gazebo message include and changes the COMMAND publisher from msgs::Double to msgs::Int32, rounding the command value. The EER_Thruster subscriber expects integer ESC values, so the message types must match for a motor topic to receive commands. The patch also makes Qt explicit and removes the connector's unrelated camera plugin build requirement for this local Mac build. It is still named after the first Beaumont experiment, but prepare_mac.sh requires it for BlueROV.

## Slide 9
generate.py: three frame definitions
FILE 5 OF 9
Frame
FRAME_CONFIG
Motors
BlueROV1
BlueROV2
BlueROV2 Heavy
0
1
2
6
6
8
Each motor row: roll, pitch, yaw, vertical, forward, sideways
Notes: Source: docs/bluerov-gazebo/generate.py lines 13–79. FRAMES holds the frame configuration number, six motor mixing factors per motor, and schematic motor positions for BlueROV1, BlueROV2, and Heavy. The factors are roll, pitch, yaw, throttle, forward, lateral in ArduSub motor order. BlueROV1 and BlueROV2 have six thrusters; Heavy has eight. This is a map between autopilot output numbers and Gazebo geometry, not measured hardware geometry.

## Slide 10
generate.py: convert axes and place motors
FILE 5 OF 9
ArduSub convention
Gazebo model convention
X: forward
Y: right
Z: down
Motor factors follow this frame.
X: forward
Y: left
Z: up
The generator flips Y and Z for positions and orients the thruster joint.
Notes: Source: docs/bluerov-gazebo/generate.py lines 98–159. ArduSub's body coordinates use x forward, y right, z down. The generated Gazebo model uses x forward, y left, z up. add_thruster converts positions and sets a joint orientation so the local +Z axis points along the intended thrust direction. motor_axis accounts for the ESC curve's command-to-force polarity. This is why a sign error can make a dive command raise the Gazebo vehicle. The static verifier checks each generated axis.

## Slide 11
generate.py: four kinds of output
FILE 5 OF 9
model.sdf Body, thrusters, IMU, connector
model.config Gazebo model metadata
world.sdf Physics, buoyancy, starting pose
frame.parm ArduSub FRAME_CONFIG value
Connector channel 0 publishes to motor_1
Notes: Source: docs/bluerov-gazebo/generate.py lines 160–303. The script writes a model.sdf for each ROV, a model.config, a world SDF, and a .parm file. The model includes a box body, IMU, thruster links, EER_Hydrodynamics, and ArduPilotPlugin. The world includes physics, buoyancy, and the model at a starting pose. The parameter file sets FRAME_CONFIG. The connector block maps ArduSub channel 0 to Gazebo motor_1, because connector channels start at zero while ArduSub motor numbers start at one.

## Slide 12
generate.py: assumptions to record
FILE 5 OF 9
Numerical assumptions
Portability assumptions
12 kg nominal mass
0.012 m³ displacement
Shared placeholder drag
Schematic thruster positions
macOS .dylib plugins
Absolute connector-library path
Generated worlds stay local
Rebuild after moving dependencies
Notes: Source: docs/bluerov-gazebo/generate.py lines 187–280 and the source package README. The body is a simple box, nominal mass is 12 kg, displaced water volume is 0.012 m³, drag coefficients are shared placeholders, and motor locations are schematic. The code hardcodes EER plugin filenames ending in .dylib and writes an absolute path to the locally built connector. This is why generated SDFs are ignored by Git. The file can establish command direction and controlled comparisons under those assumptions, not final real-vehicle performance.

## Slide 13
verify.py: compare against ArduSub
FILE 6 OF 9
Question: Do the generator’s motor factors match this ArduSub checkout?
The verifier reads AP_Motors6DOF.cpp, extracts each motor row, and compares it with generate.FRAMES.
A mismatch stops preparation before anyone records a trial.
Notes: Source: docs/bluerov-gazebo/verify.py lines 15–33 and 100–112. SOURCE_CASES maps each BlueROV model to its ArduSub source-code case. source_factors slices AP_Motors6DOF.cpp text and parses add_motor_raw_6dof calls. The script then compares the parsed factors with generate.FRAMES. This catches a generator table that no longer agrees with the checked-out ArduSub mixer. The parser depends on C++ text layout and should be updated if the source format changes. The checks use Python assert, so run normally without python -O.

## Slide 14
verify.py: wiring and possible motions
FILE 6 OF 9
Checks it performs
What rank does not prove
Motor count and channel order
Gazebo topic names
Thruster axes and positions
Idealized force direction
Allocation matrix rank
Handling performance
Controller stability
Real thruster output
Energy use
Fault tolerance
Notes: Source: docs/bluerov-gazebo/verify.py lines 35–99. For each generated model, verify_frame checks the number and order of connector controls, topic names, thruster plugins, joint positions, and rotated axes. It calculates an idealized six-component force-and-torque vector from each motor, then finds matrix rank. Expected ranks are 6 for BlueROV1 and Heavy and 5 for BlueROV2. Rank means mathematically independent motion directions in this simplified model. It does not measure control quality, stability, speed, current draw, or real hydrodynamics.

## Slide 15
run_gazebo_mac.sh: server or window
FILE 7 OF 9
bash run_gazebo_mac.sh bluerov2 server
bash run_gazebo_mac.sh bluerov2 gui
The server calculates motion. The GUI shows it. Both use the same partition name so the window finds the correct world.
Notes: Source: docs/bluerov-gazebo/run_gazebo_mac.sh lines 1–35. The script accepts one of three layouts and a part argument, server or gui. It checks that the selected world and rov-sim thruster plugin exist. It sets GZ_IP to loopback, a layout-specific GZ_PARTITION, and the model resource path. The server branch adds the rov-sim system plugin path and runs gz sim -s -r, which starts physics immediately. The gui branch runs gz sim -g. On macOS these are separate commands for the same simulation. The script does not start SITL.

## Slide 16
launch_sitl_gui.sh: connect the autopilot
FILE 8 OF 9
Layout name sets the frame and parameter file.
--model JSON connects SITL to external physics.
-I1 uses the matching Gazebo connector port.
--sysid 2 marks the vehicle in QGroundControl.
--out 127.0.0.1:14660 sends MAVLink to QGroundControl.
--use-dir keeps each layout’s logs separate.
Notes: Source: docs/bluerov-gazebo/launch_sitl_gui.sh lines 1–64. The layout selects ArduSub frame and base parameter file. The script checks .venv/bin/python, refuses to run if another SITL vehicle process is present, checks the generated parameter file, then calls sim_vehicle.py with --model JSON. -I1 matches the connector on UDP 9012. --sysid 2 identifies this vehicle in QGroundControl. -L Jervis_Bay sets the map origin. --out 127.0.0.1:14660 sends MAVLink to QGroundControl. --use-dir stores logs in a layout-specific temporary directory. The GUI still requires the user to click Launch SITL.

## Slide 17
Beaumont helper: an earlier experiment
FILE 9 OF 9
What it did
Current package decision
Copied Beaumont into an isolated test
Added eight connector channels
Corrected the IMU topic for the test
The BlueROV generator replaces this route.
No current setup script calls the helper.
Safe to unstage if historical replay is unnecessary.
Notes: Source: docs/beaumont-gazebo-prepare-test.py lines 1–95. This script copies the original Beaumont model and world to an isolated output directory, changes the world include URI, removes an explicit IMU topic, and inserts an ArduPilotPlugin block with eight controls. It proves a connector can exchange motor and sensor messages with Beaumont, but those motors do not match a stock BlueROV frame. Nothing in prepare_mac.sh, generate.py, or the BlueROV launchers calls this file. It is the one staged file that can be unstaged if the GitHub package should contain only the BlueROV route.

## Slide 18
One BlueROV2 trial, start to finish
OPERATING SEQUENCE
1 Build ArduSub SITL
2 On a fresh checkout, run prepare_mac.sh
3 Start Gazebo server, then its window
4 Launch ArduSub SITL and connect QGroundControl
5 Move one control briefly; save both data streams
6 Repeat the same trial for the other layouts
Notes: Sources: docs/bluerov-gazebo/prepare_mac.sh, run_gazebo_mac.sh, launch_sitl_gui.sh, generate.py, verify.py. First build ArduSub SITL, then prepare local dependencies and generated worlds. Start Gazebo server and optionally its GUI in separate terminals, then launch SITL and QGroundControl. Select vehicle 2 and port 14660 in QGroundControl. Use Manual mode, arm, issue one short movement, release, and disarm. Save the SITL BIN log and Gazebo pose recording under a trial ID. Repeat under the same assumed physical parameters for other layouts. These steps are for software simulation only.

## Slide 19
Review findings before using the results
CODE REVIEW SUMMARY
Keep: the generator, verifier, launchers, both required patches, and .gitignore.
Consider unstaging: the Beaumont copy helper.
Before comparing frames: run one-motor and one-axis checks for every layout, record assumptions, and save both SITL and Gazebo data.
Treat rankings as preliminary until real ROV parameters exist.
Notes: Sources: all nine staged files. The current code is appropriate for a preliminary software comparison, with limits: the full fresh Mac preparation script was not rerun in this pass; dynamic vertical checks previously covered BlueROV2 while BlueROV1 and Heavy still need direct motion checks; model dimensions and hydrodynamics are placeholders; the verification source parser is text-sensitive; and the Beaumont helper is historical. A further limitation is that generated/ is ignored and must be recreated on each Mac. No Windows integrated route was verified. These are review findings, not claims that the code is unsafe for simulation.